| Item No. | Description | Unit | Qty. | Unit FOB price Port of loading | Total FOB | Unit price C&F | Total C&F) By Sea khi | Deviation From Tender Spec if any |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | Hydraulic Truck Crane R.H.D/ L.H.D. 55 Metric Ton Capacity ( Technical Specifications As Per Annex ’A’ | Number | 04 |  |  |  |  |  |

Annexure “ABI”

TECHNICAL SPECIFICATIONS FOR TRUCK CRANE

1.	Type:			Hydraulic Truck (Telescopic Boom); Left Head/Right

Hand Drive.

2.	Nominal Lifting	55 metric tons/60 short tons (5% variation is acceptable

Capacity)

- UPPER STRUCTURE

3.1	Boom:	4-5 Section; Full power boom; Basic Boom Length   minimum 10 meters/33 feet (fully retracted) to minimum 33.5 meters/110 ft (fully extended) with boom single indicator and without jib.

3.2	Main Winch:	Grooved drum driven by hydraulic motor. Spin resistant Type wire rope equipped with wire rope guards.

3.3 	Hook Block:	            55 metric tons (60 short tons) quick reeve type.

3.4	Swing:	Continuous 360 full circle swing with smooth swing   speed equipped with swing brake and swing lock.

3.5	Hydraulic System:   Hydraulic pumps powered by carrier engine, multiple control valves actuated by pilot pressure with integral pressure relief valves. Hydraulic circuit equipped with oil cooler and returns line filters.

3.6	Operator’s Cab:	One sided on-man type cabin of steel ½” composite fibrous material and safety glass windows; Acoustically insulated Adjustable operator’s seat with  seat belt; Cab should be equipped with window wiper, audible swing alarm, fire extinguisher, sun screen, back up alarm and air conditioning system.

3.7	Controls:	Joystick type controls for swing, main winch; Boom hoist and foot controls for boom telescoping, swing brake and engine throttle based on I.S.O. standard layout. Cabin mounted automatic moment limiter with display of operating data like machine configuration, boom length, boom angle, radius of load, allowed load, actual load, percentage of allowed load, out rigger position etc.

- CARRIER

4.1	Drive:			8 x 4, Right Hand / Left Hand Drive.

4.2  	Cab:	Two men cab of steel/laminated fibrous composite material; Cab equipped  with adjustable driver seal; Fire extinguisher;  Cab air conditioner; AM/FM radio; Audio/ Visual warning system; etc.

4.3	Engine:	2/4 Stroke, Water-cooled Diesel Engine designed to meet minimum Euro-2 standards.

4.4 	Transmission:		Manual type

4.5.	Brake System	Full air service brake; should be equipped with parking brake: Exhaust brake and Emergency brake.

4.6  	Fuel Tank capacity:	Single/Dual fuel tanks having 500-800 liters total capacity.

4.7 	Steering			Hydraulic Power Assisted:

4.8	Tires	Radial tires suitable for on-road /off-road application.

4.9	Out Riggers	Four Hydraulic telescoping beam and jack out-riggers equipped with lightweight floats. Each out rigger controlled simultaneously or independently from either side of the carrier. Sight level gauges for leveling of the crane.

5.	 Books/ Manuals:	02 sets per crane each of Parts books, Operator Manuals and Workshop Manuals in printed form in English language. Parts catalogues should also be provided on Compact Disc.

6. 	Commissioning:	Commissioning of cranes to be done by the manufacturer/ supplier’s representative at OGDCL premises, Karachi Pakistan.

7. 	Financial Bid:	The financial bid should be sumi8tted by the bidder indicating the following heads separately:

7.1Price of the Truck Crane.

7.2 Price of basic hand tools.

7.3Price of two years recommended spare p[arts with description, part numbers, unit price and total price. OGDCL has the right to scrutinize the spare parts list and add or delete the quantity.

7.4. Price of manuals/ cataloguers/c.ds.

7.5. Cost of commissioning of the cranes at OGDCL warehouse in Pakistan.

8.	 Bid Evaluation:	Evaluation of financial bid will be made at the C.N.F price quoted for craned, had tools, catalogues/ manuals and the cost of commissioning of the cranes. The bid of spare parts will be evaluated separately.

9.	Warranty:	One year warranty from the date of commissioning to be provided by the manufacturer for free of cost replacement of any components/ assemblies due to malfunctioning.

9. 	Recommended Venders: 	Renowned makes from U.S.A./ Japan and Western Europe only.

NOTE:    The participants should provide an authentic document with their bid showing permission/ assurance of the concerned Government agencies for export of the offered cranes to Pakistan.

10. 	After Sale Service:	Good / reliable after sales/ Maintenance Services should be available on request.